## Slide 1: Industry 4.0 for factory automation PRESENTED BY: THIRUCHITRAMBALAM (21IM60S01) ANKIT (21IM60R06)

## Slide 2: Seminar on Industry 4.0 for Factory automation
Overview of Industry 4.0
Case study to understand effect on Industry 4.0 in welding
Problem definition/Challenges in implementation
Literature review for selected challenge
Paper presentation/ Understanding of the concept
Data collection
Analysis of data
Replicate the Mathematical modelling
Comparing the actual output to Solution output
Conclusion
Legend: Completed /Under progress /Planned ahead

## Slide 3: LITERATURE OF REVIEW
AUTHOR | SUMMARY OF WORK | Limitations
Ennsbrunner, Bruckner, Posch et al (2018) | Digitalizing welding knowledge,Modern welding power sources,Welding parameter selection and storage,Data security,Welding torch position identification,Communication between humans/welding machine,Virtual machine | Overall view for implementation in welding and no modelling or formulating of problems
Gadakh,Shinde, ,Khemnar et al. (2013) | Six decision-making problems which include selection of suitable welding parameters in different welding processes such as submerged arc welding, gas tungsten arc welding, gas metal arc welding, CO2 laser welding, and friction stir welding are considered in this paper by using MOORA method | Directly jumps into MOORA instead of comparing against different MCDM techniques

## Slide 4: LITERATURE OF REVIEW
AUTHOR | SUMMARY OF WORK | Limitations
Hozdić et al (2015) | General support in defining a development strategies and policies of its realization, Strategically oriented factors, research institutions and supporting institutions, Industrial organized development of new scientific knowledge and their direct transfer into the economy of the region. | Only application strategy in factory level
Vaidya, Ambad, Bhoshle et al.(2018) | The paper mainly focused on the concept of fourth industrial revolution, called Industry 4.0 which allows smart, efficient, effective, individualized and customized production at reasonable cost. With the help of faster computers, smarter machines, smaller sensors, cheaper data storage and transmission could make machines and products smarter to communicate with each and learn from each other. | Only elaborates on the factory level. No specific information on transforming to Industry 4.0

## Slide 5: Optimization of welding process parameters using MOORA method by V. S. Gadakh & V. B. Shinde & N. S.Khemnar Et al.
DECISION MAKING
THE MOORA METHOD
DECISION MAKING PROBLEM
CONCLUSION
LITERATURE REVIEW
REFERENCES

## Slide 6: DECISION MAKING
Simple, systematic, and logical methods or mathematical tools to guide decision makers.
The objective of any selection procedure is to identify appropriate selection criteria.
To obtain the most appropriate combination of criteria in conjunction with the real requirement.
To identify those criteria that influence an alternative selection for a given problem by using simple and logical methods.
1

## Slide 7: THE MOORA METHOD
Multi-objective optimization technique by Ratio analysis (MOORA)
Used to solve various types of complex decision making problems in the manufacturing
Process of simultaneously optimizing two or more conflicting attributes /environment
MOORA method starts with a decision matrix showing the performance of different alternatives with respect to various attributes
. Then a ratio system is developed.
  Total ratio
  Schärlig ratio
  Stopp ratio

## Slide 8: THE MOORA METHOD

## Slide 9: Decision Making Problems
1. Submerged arc welding :
Optimization of welding input parameters has always been an open research area for many researchers.
have applied the Taguchi method (TM) in combination with the grey relational analysis (GRA).
For solving multiple-criteria (objective) optimization problem in submerged arc welding.

## Slide 10: Introduction to SAW
. Arc fully submerged in fusion
. Heat loss is minimum
. The thermal efficiency is as high as 80-90%
. Produces no visible arc light
. Welding is spatter free
. High deposition
. Downhand welding process

## Slide 11: Principle of SAW
. Instead of a flux covered electrode
. Granular flux and bare electrode is used
. Arc is generally start by steel wood method
. When the welding current is switched on
. The steel wool provides a conducting path for the arc to establish
. The flux serves as shielding medium
. The process may be semi automatic or fully automatic

## Slide 12: Operating characteristics
. Flux is fed directly on the arc from a hopper
. Arc heat burns some of the flux, electrode tip and adjacent edges of the base metal
. Slag floats on the molten metal
. Slag shield results in a slower cooling rate

## Slide 13: Operating variable
. Welding current
. Polarity
. Welding voltage
. Welding speed
. Electrode diameter
. Wire feed rate
. Electrode extension
. Type of flux
. Width and depth of flux layer

## Slide 14: Operating variable
Power source
. Constant –voltage power supply
. Self regulating
Operating variable condition
. Produced by mixing the ingredients ,then melting ,cooling and grinding
. Provides smooth stable arcs , with welding currents up to 2000A
. Flux prior to use should be baked to remove moisture

## Slide 15: Operating variable condition
. Width and depth of flux
. Layers are too deep
. Layer is to shallow

## Slide 16: Welding backing
. Saw produces a large volume of highly fluid weld metal
. Methods for weld backing >
1) Backing strips
2)Backing strips
3) Copper backing
4) Flux backing
5) Gas backing

## Slide 17: Crack in SAW
.Weld metal composition
.The shape of the Weld influences the solidification pattern
.Strain on solidifying weld

## Slide 18: Advantages
. High quality welds with min. operator skills
. Minimum of welding fume and arc of visibility
. The ability to produce high quality , defect free welds

## Slide 19: Conclusion
>The selection of optimal process parameters in different welding processes using the MOORA method is presented.
>It is observed that the top-ranked alternatives almost match with those derived by past researchers.
>It can provide a better accurate evaluation of the alternatives.
>It is not so efficient when the decision matrix contains a large number of qualitative attributes.
>The method is a general method and can consider any number of quantitative and qualitative selection criteria simultaneously.

## Slide 20: Way forward plan
Select a welding process
Data collection of Welding input parameters and Output parameter – Take from paper from case study
Preparation of the decision matrix
Normalising
Providing ranking
Finding actual output
Mathematical modelling in Mat lab
Comparing the actual output to Mat lab output.
Conclusion

## Slide 21: REFERENCES
1.)Benyounis KY, Olabi AG (2008) Optimization of different welding processes using statistical and numerical approaches—a reference guide. Adv Eng Softw 39:483–496
2.) Rao RV (2007) Decision making in the manufacturing environment: using graph theory and fuzzy multiple attribute decision making methods. Springer, London
3.) Brauers WKM (2004) Optimization methods for a stakeholder society: a revolution in economic thinking by multiobjective optimization. Kluwer Academic, Boston
4.) Brauers WKM, Zavadskas EK (2006) The MOORA method and its application to privatization in a transition economy. Control Cybern 35:445–469
5. Brauers WKM, Zavadskas EK, Peldschus F, Turskis Z (2008) Multiobjective decision-making for road design. Transport 23:183– 193
6. Brauers WKM, Zavadskas EK, Peldschus F, Turskis Z (2008) Multi-objective optimization of road design alternatives with an application of the MOORA method. In: Proceedings of the 25th international symposium on automation and robotics in construction, Lithuania, 541–548
7. Brauers WKM (2008) Multi-objective contractor's ranking by applying the MOORA method. J Bus Econ Manag 4:245–255
8. Brauers WKM, Zavadskas EK (2009) Robustness of the multiobjective MOORA method with a test for the facilities sector. Technological and economic development of economy. Balt J Sustain 15:352–375

## Slide 22: REFERENCES
9. Kalibatas D, Turskis Z (2008) Multicriteria evaluation of inner climate by using MOORA method. Inf Techol Con 37:79–83
10. Brauers WKM, Zavadskas EK (2010) Project management by MULTIMOORA as an instrument for transition economies. Technological and economic development of economy. Balt J Sustain 16(1):5–24
11. Chakraborty S (2010) Applications of the MOORA method for decision making in manufacturing environment. Int J Adv Manuf Technol 54(9–12):1155–1166
12. Chakraborty S (2010) A decision making framework for selecting non-traditional machining processes using the moora method. In: Proceedings of the 4th international conference on advances in mechanical engineering, Sept. 23–25, 2010 S.V. National Institute of Technology, Surat 395 007, Gujarat, India.
13. Gadakh VS (2011) Application of MOORA method for parametric optimization of milling process. Int J Appl Eng Res 1(4):743–758
14. Lootsma FA (1999) Multi-criteria decision analysis via ratio and difference judgement. Springer, London
15. Datta S, Bandyopadhyay A, Pal PK (2008) Solving multi-criteria optimization problem in submerged arc welding consuming a mixture of fresh flux and fused slag. Int J Adv Manuf Technol 35:935–942
16. Tarng YS, Yang WH (1998) Optimisation of the weld bead geometry in gas tungsten arc welding by the Taguchi Method. Int J Adv Manuf Technol 14:549–554

## Slide 23: REFERENCES
17. Holimchayachotikul P, Laosiritaworn W, Jintawiwat R, Limcharoen A (2007) Optimization of gas metal arc welding parameters for ST 37 steel using support vector regression. The IE network conference 24– 26 October 2007
18. Park YW, Rhee S (2008) Process modeling and parameter optimization using neural network and genetic algorithms for aluminum laser welding automation. Int J Adv Manuf Technol 37:1014–1021
19. Dinaharan I, Murugan N (2012) Optimization of friction stir welding process to maximize tensile strength of AA6061/ZrB2 insitu composite butt joints. Met Mater Int 18(1):135–142
20. Kalaiselvan K, Murugan N (2012) Optimizations of friction stir welding process parameters for the welding of Al-B4C composite plates using generalized reduced gradient method. Procedia Eng 38:49–55